## Slide 1: Single DSP (Single Core)
Block Diagram
L
EMI, Bridge
& Inrush, limiter
CCM Classical
PFC
Half bridge LLC
Resonant tank & Transformer
SR MOSFET
& Driver
Output filter
OUTPUT 12V POWER CONNECTOR
dsPIC33EP128GS706/TQFP
LLC HB control ,SR control, Secondary sense and protection, MSI with slave Core, PM Bus communication
PFC control, Relay Control, AC sense and protection, MSI with master core, Temperature protection, FAM control
Current sense
Isolated driver
Aux. fly- back
STANDBY POWER CONNECTOR
N
E
PM BUS CONNECTOR
Oring
Isolated barrier
Bulk cap
PGND
SGND
UCC27511

## Slide 2: (Dual Core) Single DSP Function Block
System
GPIO
GPIO
ADC
PWM
ADC
Master Slave Interface Register with Isr
PWM
dsPIC33CH 128MP508
SR
PWM_GD
Control_1
Control_1
Control_1
Control_1
12V_REF
LED1_PWM
FAN_PWM
RESERVED
STB_ADJ
12V_Vout
12V_Iout
12V_Vout
RELAY_CTL
IPFC_DET
VSB_Vout
VSB_Iout
VSB_RS
12V_CS-
12V_CS+
T_AIR
T_INLET
T_RESERVED
VAC_N_DETECT
VAC_L_DETECT
VPFC_DET
VPFC_OVP_DET
IPFC_REPORT
PWOK
ALERT
STB_EN
  Capture
Comparater
12V_IO
FAN_RPM
EEPROM
PM IC
I2C/PMBUS
UART
PMBUS
I2C
PS_KILL
PS_OK

## Slide 3: (Dual Core) Single DSP Function Block
Tasks
AC Brown In /Out control
Relay control
Adaptive VBulk & Fsw
PFC control
Current Limit
Bulk OVP
AC input OVP
Temperature sensors
Primary Info Reporting
Power On/Off Sequence
Bootloader
V12(Vref) &VSB Protection
DCDC control
Current Share
Fan control
LED control
Calibration and Event Log
Master Slave Interface control
UART Communication
PMBus

## Slide 4
Thank You Q & A